## Slide 1
Aircraft-Engine Remaining Useful Life Prediction
Comparative Evaluation of Random Forest, XGBoost and LSTM
NASA C-MAPSS FD001 Dataset
MSc Data Science & Artificial Intelligence
Dissertation Presentation

## Slide 2
1. Background and Motivation
2
The problem
Aircraft engines vary in operation and are often subjected to different conditions. Being able to predict when the engine's useful life is drawing to a close would help in scheduling maintenance works.
Why RUL?
Remaining Useful Life (RUL) is a measure of an engine's remaining expected life before breakdown or the time of its life cycle end.
Research focus
The dissertation is evaluating FD001 by comparing machine learning algorithms to LSTM-based model.
Core idea
Sensor data
→
Preprocessing
→
RUL target
→
ML models
→
Evaluation

## Slide 3
2. Aim, Objectives and Research Questions
3
Aim
Assessing machine-learning methods for estimating the remaining useful life of aircraft engines through the use of NASA C-MAPSS FD001 data.
Objectives
Carried out a comprehensive comparison of machine-learning approaches for aircraft-engine remaining-useful-life (RUL) prediction using NASA C-MAPSS FD001.
Fetched, formatted and pre-processed FD001 sensor data for the experiments.
Designed the RUL target and laid out an experiment plan for reproducibility.
Machine learning: Random Forests, XGBoost and LSTM.
Models have been evaluated from the standpoint of MAE, RMSE, R², and NASA PHM08 scores.
From results interpretation, limitations have been pointed out.
Research question
Which of the evaluated models provides the strongest RUL prediction performance on FD001 under the defined experimental setup?

## Slide 4
3. Literature Review and Research Gap
4
Traditional ML
Methods such as Random Forest and boosting which are based on tree algorithms can learn nonlinear relationships even from features created by the user or from a database with few attributes only (tabular features).
Deep learning
LSTM networks are a special kind of feed forward neural network architecture specifically created to deal with sequential data. They have memory features that allow them to track temporal dependence of sequential data from sensors.
Gap addressed
The research offers a fair comparison of RF, XGBoost and LSTM methods through the same evaluation set and using FD001 data as a benchmark
The most vital point to highlight in the presentation is that model performance is a function of many factors besides the algorithm. The data preparation as well as the target construction and evaluation design will have a major influence.

## Slide 5
4. Dataset: NASA C-MAPSS FD001
5
Training set
20,631 records × 26 columns
Test set
13,096 records
Test RUL
100 final RUL values
FD001 illustrates just the one scenario of the system in motion while the machine is malfunctioning.
During the whole engine run cycles, data from the sensors are kept.
To sum up, after excluding some of those sensor inputs and settings, only sensor inputs or features were used.
Only up to 456 RUL was considered so as to minimize the impact from too large targets at early-life stage.

## Slide 6
5. Research Methodology
6
FD001 data
→
Cleaning
→
Feature selection
→
RUL construction
→
Train/validation
→
RF / XGB / LSTM
→
Metrics
Experimental principle
An engine-level validation split with 80/20 proportion was carried out at random.
Tree models rely on engineered or tabular representations.
LSTM is built upon fixed-length input sequences.
We compared different models fairly since they used the same metric, reported performance.

## Slide 7
6. Data Preprocessing and Experimental Design
7
Feature handling
Dropped setting 3 and sensors 1, 5, 10, 16, 18 and 19; 17 features retained.
Target construction
RUL values were derived from engine cycle information and capped at 125.
Sequence design
LSTM input used a sequence length of 30 cycles.
Reproducibility settings
Random state: 42
Validation: 80/20 engine split
CPU-only experiment
Results saved under: results_fd001
Evaluation metrics
MAE
RMSE
R²
NASA PHM08 score

## Slide 8
7. Models Used
8
Random Forest
Ensemble of decision trees.
Advantages: good for tabular data, reliable baseline.
XGBoost
Gradient-boosted
decision trees.
Advantages: through boosting step by step, it can learn complex nonlinear patterns.
LSTM
Long Short-Term Memory network. Architecture used: 64/32 LSTM units, dropout 0.2, dense 16; up to 50 epochs with early stopping patience 8.

## Slide 9
8. Results: Random Forest
9
Random Forest performance
MAE
12.5250
RMSE
17.4180
R²
0.6011
PHM08
190,859.91
Interpretation
Provide a good nonlinear baseline.
R² shows that a large part of RUL variation is captured.
Performance was weaker than the LSTM results reported for the selected metrics.

## Slide 10
9. Results: XGBoost
10
MAE
12.2332
RMSE
17.4143
R²
0.6013
PHM08
231,988.13
Interpretation
MAE is slightly lower than Random Forest.
R² is very close to Random Forest.
The reported PHM08 score is higher than Random Forest in the dissertation results.

## Slide 11
10. Results: LSTM
11
MAE
10.7976
RMSE
15.9693
R²
0.7114
PHM08
72,247.63
Interpretation
Lowest MAE and RMSE among three tested models.
Best R² reported in the experiment.
Lowest stated NASA PHM08 score, which means it was the weakest one at that metric according to that work.

## Slide 12
11. Comparative Evaluation
12
Model | MAE | RMSE | R² | PHM08
Random Forest | 12.5250 | 17.4180 | 0.6011 | 190,859.91
XGBoost | 12.2332 | 17.4143 | 0.6013 | 231,988.13
LSTM | 10.7976 | 15.9693 | 0.7114 | 72,247.63
Main result
Across the reported metrics, the LSTM achieved the strongest overall performance in this FD001 experiment.

## Slide 13
12. Discussion and Key Findings
13
With respect to MAE, LSTM performed better than the tree models: 10.7976, to 12.5250 for Random Forest, and 12.2332 for XGBoost.
Also, the highest R² value 0.7114 was reported by the LSTM model with an approximate 0.60 by each tree model.
The outcomes are in favor of the sequential modeling technique to predict the temporal sensor pattern represented in data from FD001 sensor.
it's true that both Random Forest and Gradient Boosted Trees models are capable of giving results that do not significantly differ from those of the first-class methods in tabular data processing.
At the same time, they take less time to run which is very convenient, especially when it comes to simpler problems.
The analysis was mainly based on the dataset FD001 and the experimental methodology described in this work.

## Slide 14
13. Practical Implications and Limitations
14
Practical implications
•RUL prediction enables you to plan the condition based maintenance more effectively.
•If deterioration is detected early, you have enough time to arrange resources for inspection and maintenance.
•When selecting model types, predictive accuracy, computational cost, and deployment constraints are some of the factors that should be prioritized.
Limitations
• Evaluation was performed exclusively on NASA C-MAPSS FD001.
• FD001 is the case of a highly controlled simulation, not actually representative of a full-scale fleet in the real world.
• The study was limited to evaluating three methods only, namely, RF (Random Forest), XGBoost, and LSTM (Long Short-Term Memory)
• Performance results are influenced by pre-processing steps, chosen features, RUL (Remaining Useful Life) cap limits, and cross-validation design.

## Slide 15
14. Conclusion and Future Work
15
Conclusion
The study came up with an RUL prediction pipeline, which was tested and verified in different runs and gave the same results for NASA C-MAPSS FD001.
In the study, Random Forest (RF) and XGBoost were found to be good representatives of conventional ML methods.
The Long Short-Term Memory (LSTM) model yielded the best-performing results for most of the metrics used in this study, that is, MAE, RMSE, R², and PHM08.
Future work
Evaluate new C-MAPSS operational conditions plus failure situations.
Do research on better design of sequence models as well as finding the best parameters (hyper parameter optimization).
Check the model performance on the data collected in real life from engine-monitoring.
Explore RUL forecasts that are aware of uncertainty for helping maintenance decision making.